## Slide 1
THE FUTURE ENVELOPE
TOWARDS ZERO CARBON BUILDINGS
15‐16 December 2022 Bolzano/Bozen
Sustainability as a design parameter: tools, metrics, know-how
Claudia Di Noi
GreenDelta GmbH, Berlin, Germany
Organized by
Sponsors
Collaborations

## Slide 2
Classification system to guide sustainable investments
Highly affecting the building sector (directly and indirectly): new construction, renovation, installation, maintenance and repair, and acquisition & ownership
Life Cycle Assessment of the whole building according to Level(s) and EN15978 is required to comply with circular economy criteria
Demand for sustainability: the EU Taxonomy
https://finance.ec.europa.eu/sustainable-finance/tools-and-standards/eu-taxonomy-sustainable-activities_en
https://environment.ec.europa.eu/topics/circular-economy/levels_en

## Slide 3
Life Cycle Assessment (LCA)
Huang, B. et al. (2020) A Life Cycle Thinking Framework to Mitigate the Environmental Impact of Building Materials https://doi.org/10.1016/j.oneear.2020.10.010
Methodology for quantification of environmental impacts of products, processes and services across the life cycle
Based on standards:
ISO 14040, ISO 14044
EN 15804 (construction products)
EN 15978 (buildings)
…

## Slide 4
Sustainability should not be isolated from the technical building envelope performance
How to integrate sustainability assessment in the design process and benefit from it?
How to tackle complexity of sustainability
Tool development for data management and sustainability assessment
Sustainability metrics
Know how: Sustainability consultancy and research, and capacity building

## Slide 5
Tools

## Slide 6
Impacts and risks need to be calculated across the life cycle
Professional LCA software, free or licensed
LCA calculators (e.g. spreadsheets, )
LCA screening tools (e.g. spreadsheets, rating 1-5)
LCA software linked to a Common Data Environment (e.g. BIM)
Frontiers of LCA software: link with Artificial Intelligence
…
Calculation of building LCA

## Slide 7
Lack of representative data and benchmarks is one of the main challenges when performing sustainability assessment of buildings
Common data sources (not exhaustive):
Generic LCA databases with building products: ecoinvent, GaBi, PEF…
Standardized LCA database of building products: Ökobaudat (DE)
Environmental Product Declarations: reports of LCA of specific construction products (usually as PDFs, but can be added to some LCA software: One Click LCA and openLCA)
Collecting construction data for LCA
https://nexus.openlca.org/databases
https://www.oekobaudat.de/

## Slide 8
Construction materials database, provided by the German Federal Ministry of Transport, Building and Urban Development
13,000 datasets representing EPDs
Example 1: Ökobaudat in openLCA
https://nexus.openlca.org/database/%C3%96kobaudat

## Slide 9
Calculate life cycle stages (production, transport, use, end of life…)
Combine datasets to create your own case studies (building components or full buildings)
Example 1: Ökobaudat in openLCA
https://nexus.openlca.org/database/%C3%96kobaudat

## Slide 10
End of life is one of the most uncertain stages of building component life cycles
Construction and demolition waste is a major problem (1/3 of all waste in EU)
Proposal: combining a digital product description – the “Digital Product Passport”– with intelligent sorting technologies supported by artificial intelligence (AI)
Example 2: LCA and artificial intelligence tool
https://environment.ec.europa.eu/topics/waste-and-recycling/construction-and-demolition-waste_en
Notes: Example: the materials used in the manufacturing processes and their properties are stored in the life cycle record and made available for material recovery – i.e. for sorting, recycling, and subsequent reuse.

## Slide 11
Example 2: LCA and artificial intelligence tool
https://www.recirce.de/
© Fraunhofer IWKS
Digital Product Passport
Materials
Joining techniques
Disassembly effort
Harmful materials
Durability
Users
….
Sorting plant
Artificial Intelligence
1. Sorted waste
2. Best end of life pathway
LCA tool to calculate impacts of different end of life pathways
Waste
Product

## Slide 12
Metrics

## Slide 13
Areas of protection
Resource depletion
inventory
Σ commodity
Σ Land use
Σ CO2
Σ HFE
Σ P
Σ SO2
Σ NOx
Σ CFC
Σ Cd
Σ PAK
Σ DDT
…
Land use
Global warming
Acidification
Eutrophication
Ecotoxicity
Human-toxicity
…..
Ozone depletion
Damage of resources
Damage of ecological system
Damage of health
…..
Impact assessment methods: Environmental Footprint, Recipe, CML…

## Slide 14
Metrics beyond carbon and LCA indicators
Circularity: Material Circularity Indicator (Ellen MacArthur Foundation), Circularity Index (Cullen, 2017)
Criticality: raw materials important for the EU economy but with high supply risks (e.g. PV cells)
Costs: Life Cycle Costing
Social impacts and risks: Guidelines for social Life Cycle Assessment of Products and Organizations (UNEP/2020)
https://ellenmacarthurfoundation.org/
Cullen, Jonathan M. 2017. “Circular Economy: Theoretical Benchmark or Perpetual Motion Machine?” Journal of Industrial Ecology 21 (3): 483–86. doi:10.1111/jiec.12599.
United Nations Environment Programme (2020). Guidelines for Social Life Cycle Assessment of Products and Organisations 2020. https://wedocs.unep.org/20.500.11822/34554
https://nexus.openlca.org/databases

## Slide 15
Know-how

## Slide 16
Life Cycle Assessment in practice
Application of LCA for the design of building envelopes for renovation
H2020 EU project: INFINITE (2020-25)
Industrialized retrofitting principles:
OFF-SITE PREFABRICATION
MULTI-FUNCTIONAL ENVELOPE
DIGITALIZATION
3 case studies (residential buildings):
ITALY
SLOVENIA
FRANCE
Green envelope
Energy and fresh air distribution
Smart glazing
Solar-thermal generation
Photovoltaic energy generation
BIM
Building management
https://infinitebuildingrenovation.eu/

## Slide 17
The Italian case
Location: Greve in Chianti, Tuscany, Italy
Destination: social housing
2 twin buildings with 4+4 dwellings
Year of edification: 1978-79
Reinforced concrete frame structure
Autonomous heating and domestic hot water systems
Number of residents: 15
Residents: elderly, retired (most residents have lived there for 30-40 years)

## Slide 18
Comparative LCA: industrialized vs traditional retrofit
Traditional and industrialized retrofit need to achieve the same function: providing a living environment to the inhabitants of the Italian demo building over a reference study period of 50 years and achieving the following performance:
Parameter | Value | Unit
Indoor air temperature (winter) | 19-21 | °C
Indoor air temperature (summer) | 25-27 | °C
Indoor humidity | 30 winter, 50 summer | %
Max CO2 concentration | 1000 | ppm
Illuminance |  | lux
Self-sufficiency | 48 | %
Notes: (These are the characteristics that need to be achieved by all compared renovated buildings, either with materials or with additional energy use)

## Slide 19
Setting a comparative LCA study: data collection
Industrialized retrofit: primary data from technology providers and energy simulations
Traditional retrofit: bill of quantities adapted to the specific building
 | Industrialized retrofitting | Traditional retrofitting
Envelope | Timber-based insulated façade (ventilated) Timber-based insulated roof (ventilated) New windows | Insulated façade (ventilated) Insulated roof (ventilated) New windows
Systems | Centralized heat pump Semi-decentralized ventilation, heating and cooling per dwelling PV panels (integrated in roof and façade) Solar thermal panels (integrated in façade) | Centralized heat pump connected to split units per dwelling Centralized ventilation PV panels (roof)

## Slide 20
Life cycle stages
Component production
Component assembly off-site
Installation on-site
Component production
Installation on-site
Operation
Maintenance
End of life
Operation
Maintenance
End of life
Raw materials
Raw materials
Manufacturing
Manufacturing
Industrialized retrofit
Traditional retrofit

## Slide 21
LCA results (starting point)
Chart: Environmental impacts (selected) of retrofitting
| Climate change | Ecotoxicity, freshwater | Human toxicity, cancer | Human toxicity, non-cancer | Land use | Resource use, minerals and metals | Water use
Industrialized | 1 | 1 | 0.97791 | 1 | 1 | 1 | 1
Traditional | 0.93612 | 0.87393 | 1 | 0.89701 | 0.56656 | 0.8994 | 0.98247
The higher the worse
Software: openLCA
Database: ecoinvent 3.8 cut-off
Method: EF 3.0
*Results referred to 1 building, reference life time: 50 years

## Slide 22
Life cycle stage contribution
Chart: Resource use, non-fossil [kg Sb eq.]
| Industrialized | Traditional
Manufacturing | 2.7254 | 2.5326
Transport | 0.01241 | 0.00762
Installation | 1.7854 | 1.7854
Operation | 1.1689 | 1.3168
Maintenance | 8.5634 | 7.4219
End of life | 0.01276 | 0.00554
*Results referred to 1 building, reference life time: 50 years
Chart: Climate Change [kg CO2 eq.]
| Industrialized | Traditional
Manufacturing | 75437.9 | 80055.3
Transport | 3564.4921 | 2189.1247
Installation | 7929.4139 | 8520.4699
Operation | 120650 | 135912
Maintenance | 112594 | 76837.9
End of life | 11793.5 | 7248.2051

## Slide 23
Chart: 
| Manufacturing | Transport | Installation | Operation | Maintenance | End of life
 | 0.2272 | 0.0107 | 0.0239 | 0.3634 | 0.3392 | 0.0355
Chart: 
| PVs | Timber-based facade | Timber-based roof | Ventilation | Solar thermal panels | Windows | Transport | Heat pump system | PV and ST installation | Other | Electricity | Kit replacement | System replacement | Building maintenance | Kits EoL | Systems EoL
 | 0.071 | 0.0737 | 0.0298 | 0.0096 | 0.0242 | 0.0175 | 0.0107 | 0.0085 | 0.0119 | 0.0035 | 0.3634 | 0.2459 | 0.0886 | 0.0047 | 0.0219 | 0.0136
Industrialized retrofit impacts/ analysis
Carbon footprint contributions
*Results referred to 1 building, reference life time: 50 years

## Slide 24
Where to improve in industrialized design?
1. Alternative materials
2. Technological improvement over time
4. Design for assembly and disassembly
Technology installation
Use
Maintenance
Technology EoL
Raw materials acquisition
Technology production
Life cycle stages
3. Extended service life
Pathways
5. Refine energy simulations

## Slide 25
Testing the pathways
Pathway 3: extended service life -> increased service life of solar panels (10->25 years)
Chart: Environmental impacts of building life cycle
| Climate change | Human toxicity, cancer | Water use
Industrialized | 1 | 0.97791 | 1
Traditional | 0.93612 | 1 | 0.98247
Industrialized (higher service life solar panels) | 0.93329 | 0.91342 | 0.96719
*Results referred to 1 building, reference life time: 50 years
Pathway 1: alternative material-> change compensation layer in timber façade (stone wool -> wood fibre)
Chart: Production of timber based facade/alternative compensation layer impacts
| Climate change | Human toxicity, cancer | Resource use, minerals and metals
Timber facade with stone wool | 1 | 1 | 1
Timber facade with wood fibre | 0.92945 | 0.9376 | 0.91209
*Results referred to 1 m² of timber façade, without cladding

## Slide 26
Conclusions and the way forward
We have tools and metrics, we need to apply them
Empower AEC professionals
Empower countries (e.g. national databases)
Work on communication of results
Work on setting benchmarks
Connect sustainability research with industry
The European Green Deal: “Companies making ‘green claims’ should substantiate these against a standard methodology to assess their impact on the environment”.

## Slide 27
Contact: Claudia Di Noi, dinoi@greendelta.com
GreenDelta GmbH Kaiserdamm 13, 14057 Berlin, Germany www.greendelta.com